Distributed Oscilloscope over
White Rabbit network
Author
Miłosz Malczak
Supervisor
dr inż. Grzegorz Kasprowicz

---
Motivation
Motivation
Providing a system for monitoring signals located over large distances
Disadvantages of current solutions:
- custom-made,
- not scalable,
- not precise enough,
- lack of compatibility.

---
Existing solutions
LAN-based eXtensions for Instrumentation (LXI)
  - Standardizes access to various types of laboratory instrumentation
  - Synchronization based on IEEE 1588-2002 Precision Time Protocol (PTP)
OASIS
  - Currently used at CERN for monitoring signals
  - Triggers distributed over coaxial cables
  - Provisional compensation
  - Costly, lack of proper synchronization

---
Distributed Oscilloscope

---
White Rabbit Trigger Distribution (WRTD)
Distribution of the timestamps
Possibility of compensation for logical latencies and cable lengths
Information about the delay between the triggers
Introducing delays

---
White Rabbit Network
125 MHz clock
Subnanosecond precision
Information about transmission delays over the fiber
Sending data packets

---
White Rabbit Trigger Distribution block
Local in
  - Time to Digital Converter (TDC)
  - ADC producing timestamp on threshold
Local out
  - Fine Delay Generator
  - WRTD enabled ADC
Remote in/out
  - Connection with other WRTD blocks

---
Triggers in Distributed Oscilloscope
Synchronized triggering of ADCs:
Programming the time when the ADCs should be triggered
Triggering the ADCs based on the timestamp received from the other ADC.

---
WRTD in Distributed Oscilloscope
∆ti>=δi
∆ti — delay introduced by WRTD
δi — propagation delay of the network
presamples = presamplesrequired+ ∆t *fs
postsamples = postsamplesrequired - ∆t *fs

---
Done
Done
To do
- adding support for WRTD
- making Distributed Oscilloscope more generic
- adding support for different ADCs
- adding support for TDCs
- providing common interface for different types of devices
- possibility to display White Rabbit network topology in the form of a graph
- locking ADCs sampling clock to the White Rabbit clock
- adding support for ADCs without a host
basic Distributed Oscilloscope
possibility of specifying time of the trigger